| XCOM 760 vs Microair Comparison |
| --- |
|  | XCOM 760 | Microair760 |
| Price inc gst | $A1395 | $A1295 |
| Intercom | Full VOX Intercom | Hot Mike |
| Music Input | Yes | No |
| Dual Watch (Monitor both active and standby) | Yes | No |
| Individual PTT Switching | Yes | No |
| Digital Controls | Yes | No |
| Adjustable Squelch Thresholds | Yes | Yes |
| Memory Channels | 99 | 25 |
| Voltage Monitoring | Yes | No |
| Internet Software Upgrades | Yes | No |
| Backlight LCD | Yes | Yes |
| Backlight Controls | Yes | No |
| Display | 2 line Alpha/Numerical | 2 line numerical |
| Transmit Power |  |  |
| Power Output Carrier | 6w | 3.5w |
| Power Output PEP | +20w pep | 12w pep |
| Dimensions |  |  |
| Dimensions Width | 61 | 65 |
| Dimensions Height | 61 | 59 |
| Dimensions Length (without connector) | 128 | 135 |
| Dimensions Length (with connector) | 148 | 170 |
| Weight | 403 grams | 423 grams |
| Frequency |  |  |
| Receive VOR Channels (Audio only NO Nav) | 108.000 - 117.875 | No |
| Airband Frequency Range | 118.000-136.975 | 118.000-136.975 |
| Extended Receive FM | 137.000 - 163.000 | No |
| CAP, MARS, 2m Transceive (Optional) | 140.000 - 144.000 | No |
| NOAA Weather Channels | Yes | No |
| Frequency Channels | 2200 | 760 |
| Channel Spacing | 25 kHz | 25 kHz |
| Power Supply |  |  |
| Supply Voltage | 8.0V-17V | 13.8V-16.0V |
| Minimum Voltage | 10.0V | 10.5V |
| Standby Current | <70mA | 87mA |
| Transmit Current | 2A | 1.2A |
| Stuck Mike Timer | Yes | No |

Want to know more ? Do you want to see the XCOM 760 in operation ? Well now you can by using our interactive online demonstration.

This is an exceptional sales tool that will allow potential

The XCOM's key features are included below.... Built-In VOX Intercom Worlds Smallest & Lightest VHF Com Dual Watch Monitor active & standby channels Extended Receive Range Music Input with Auto Fade NOAA Weather Channels USA 121.5 Emergency Channel Priority 6 Watt Carrier Output 20 Watt PEP Output Large Backlight LCD 99 Memory Channels Large Buttons - Easy Operation 12 Month Replacement Warranty 3 Year Optional Warranty